## Slide 1
Solar Home System
Standard Specification
(Draft for Discussion )
Ministry of Livestock, Fisheries and Rural Development
Department of Rural Development
Place - Sule Shangri-La Hotel Date- 4 - 12 - 2015

## Slide 2
System-1
Minimum power of solar PV array: 30Wp
Minimum battery storage capacity : 12V/20Ah (Lead-acid)(50%DoD)
                : 12V/12Ah (Li-ion)(90% DoD)
Charge controller : 12V/2A (PWM type)
Minimum DC LED lumens: 240 Lumens ( 80lumen/watt)- 3nos -3.5hr
DC socket outlet : USB type ( for cell-phone charging – 2.5hr)
12V/2A DC socket outlet: 15W DC TV (1.2hr)
A wiring kit of appropriate size for All DC wiring
Balance of system materials including: mounting structure, battery box, battery fuse, cabling, light switches, User Manual and O&M manual

## Slide 3
System-2
Minimum power of solar PV array: 45Wp
Minimum battery storage capacity : 12V/30Ah (Lead-acid)(50%DoD)
                : 12V/16Ah (Li-ion)(90% DoD)
Charge controller : 12V/3A (PWM type)
Minimum DC LED lumens: 240 Lumens ( 80lumen/watt)- 4nos -4hr
DC socket outlet : USB type ( for cell-phone charging – 2.5hr)
12V/2A DC socket outlet: 15W DC TV (1.8hr)
A wiring kit of appropriate size for All DC wiring
Balance of system materials including: mounting structure, battery box, battery fuse, cabling, light switches, User Manual and O&M manual

## Slide 4
System-3
Minimum power of solar PV array: 60Wp
Minimum battery storage capacity : 12V/40Ah (Lead-acid)(50%DoD)
                : 12V/23Ah (Li-ion)(90% DoD)
Charge controller : 12V/5A (PWM type)
Minimum DC LED lumens: 240 Lumens ( 80lumen/watt)- 5nos -5hr
DC socket outlet : USB type ( for cell-phone charging – 2.5hr)
12V/2A DC socket outlet: 15W DC TV (3hr)
A wiring kit of appropriate size for All DC wiring
Balance of system materials including: mounting structure, battery box, battery fuse, cabling, light switches, User Manual and O&M manual

## Slide 5: PV modules
Certification standards
Crystalline Modules: Mono-crystalline , Poly-crystalline
IEC 61215 (2005-04),IEC 61646 certified module, ISO 9001 certification
Crystalline Modules have 36 cells for 12V batteries
Tolerance of rated output of PV modules offered shall be positive only
Warranty: 10 years

## Slide 6: Continue - PV modules
Solar Module shall be warranted to produce at least 80% of rated peak watt output for at least 10 years.
Solar module should have a full replacement warranty if it fails within one year due to manufacturing or material defect.
The module shall be labeled indicating at a minimum Manufacturer, Model Number, Serial Number, Peak Watt Ratting, Voltage and Current at peak power, Open Circuit Voltage and Short Circuit Current of each module.

## Slide 7: Batteries
Certification standards
IEC 61427 Ed. 2.0 (2004-05), IEC 60896-11; Ed 1.0 (2002), IEC 60896-21 and 22 Ed 1 (2004) ,ISO 9001
Certificates or equivalent standards i.e IEEE, may be proposed by suppliers
Lead-acid: deep-cycle, heavy-duty, tubular positive plate, with immobilized electrolyte and valve regulated operation(75%) loadshed DoD)
Lead-acid: deep-cycle, heavy duty, tubular positive plate with vented and flooded electrolyte cell(75% loadshed DoD)
Li-ion : deep-cycle, heavy-duty, sealed( 90% maximum loadshed DoD)

## Slide 8: Continue- Batteries
Battery capacity shall not be less than 80% of rated capacity over a period of 18 months
12V Lead acid battery wet weight of at least 0.35kg per rated ampere-hour(C/10rate)(eg. 58Ah battery must weigh at least 58 x 0.35 = 20.3 kg)
Battery cycle life at 50% daily depth-of-discharge (DOD) must exceed 1,800 cycles
Battery shall offer at least a four year useful life

## Slide 9
The battery shall be housed in a vented compartment.
All parts of the compartment subject to battery acid contact shall be acid resistant.
This compartment shall be built strong enough to accommodate the weight of the battery.
Fig 2.Sample of Battery

## Slide 10: Charge controller
Certification standards
EC 62509 Ed.1, IEC 62109, IEC 62093 Ed.1.0, IEC 17025, IECEE standard, ISO 9001 certified manufacturer
Solid state photovoltaic charge controller, Pulse Width Modulated(PWM) regulation
Controller shall have a charging regime applicable to battery with voltage setpoints preset at factory
Controller shall have LED indicator lights or meter to show state of charge and when the battery is in a charging mode
Controller shall have protection against short circuit of input and output terminals as well as reverse polarity protection

## Slide 11
Charge Controller configuration
fig. Sample of charge controller
Electronic automatically resettable cut-offs are required-
mechanical fuses are not acceptable
Controller shall be able to safely accept 125% of the module
open-circuit voltage when battery is removed

## Slide 12: LED luminaires
Certification standards:
Compliant with Lighting Global Standard, ISO 9001
DC LED lights has at least 240 lumens
Minimum lumen efficiency of LED light should be 80 lumen/watt
Provide minimum 90% of initial lumen output after 2,000 hours or 95% after 1,000 hours
Increase in temperature of heat sink should not be more than 20ﹾCelsius after one hour operation
Color of LED light shall be white
LED light should be place at a height more 8 feet from ground
Each light shall be controlled by a separate switch

## Slide 13
Technical specifications for
public facilities
( Draft for Discussion )
Ministry of Livestock, Fisheries and Rural Development
Department of Rural Development
Place - Sule Shangri-La Hotel Date - 4 - 12 - 2015

## Slide 14
Minimum size of components for Public Facilities
Description | Design load grouth (Wh/day) | Minimum PV array (Wp) | Mimimum Battery (Ah@C20@V) |  | Battery DoD | MinimumCharge controller | Minimum Inverter (VA) | Battery Fuse | Led (Qty)
School -1 classroom | 257 | 120Wp | 55Ah | 24V | 75% | 6A | 100VA | 6A | 9
School -2 admin+1 classroom(20’x24’) | 726 | 310Wp | 150Ah | 24V | 75% | 16A | 216VA | 16A | 14
School-3 Admin+ 2 rooms(20’x24’) | 897 | 375Wp | 190Ah | 24V | 75% | 20A | 306VA | 20A | 20
School-4 Admin+3rooms(20’x24’) | 1154 | 475Wp | 240Ah | 24V | 75% | 25A | 408VA | 25A | 26
School-5 Admin+3rooms(30’x24’) | 1411 | 575Wp | 400Ah | 24V | 75% | 30A | 533VA | 30A | 34
School-6 Admin+4rooms(30’x24’) | 1668 | 675Wp | 350Ah | 24V | 75% | 35A | 658VA | 35A | 43
School-7 Admin+5rooms(30’x24’) | 1925 | 775Wp | 400Ah | 24V | 75% | 40A | 783VA | 40A | 52
Rural health centre | 692 | 280Wp | 150Ah | 24V | 75% | 15A | 250VA | 15A | 14
Sub-rural health centre | 432 | 180Wp | 90Ah | 24V | 75% | 9A | 150VA | 10A | 6
Streetlight | 147 | 70Wp | 26Ah | 12V | 90% | 6A | NA | 8A | 1
Pagoda lighting | 383 | 180Wp | 90Ah | 24V | 75% | 9A | 100VA | 9A | 9
1 x dormitary or ward | 206 | 120Wp | 55Ah | 24V | 75% | 6A | 100VA | 6A | 3

## Slide 15
School -1 1 classroom (Example)
Design load demand: 275Wh/day
Minimum power of solar PV array: 120Wp
Minimum battery storage capacity : 24V/55Ah (75%DoD-,fuse 6A )
Charge controller : 24V/6A (PWM type)
Inverter: 100VA (sine wave inverter)
AC interior LED : 720 lumen (strip luminaries-8 nos)
AC exterior LED: 550 lumen ( bulkhead luminaries- 1nos )
A wiring kit of appropriate size for All DC and AC wiring
Balance of system materials including: array mounting structure, battery box, battery fuse, AC distribution board, AC earthing, light switches, AC socket points, User Manual and O&M manual

## Slide 16
Public streetlight systems
Design load demand: 147Wh/day
Minimum PV array: 70Wp
Minimum Battery: 12V, 26Ah
Minimum charge controller: 12V, 6A
DC LED lamp: 1 nos, at least 1200lumens(12W), minimum 100lumens/watt
25,000 hour life to 80% of initial lumen output.
Li-ion batteries are preferred. Battery life is at least 1500 charge-discharge cycles or 4 years.
Battery capacity for on-time of a full 14 hours per day
Streetlight unit shall switch on automatically at night and off during daylight hours
The controller should control load switching using daylight sensing
Concrete or wooden pole shall be suitable for mounting of luminaire at the sepecifie 5m heigh above ground level

## Slide 17
Continue- Public streetlight systems
Integrated housing for complete streetlight unit:
Integrated housing for the lamp, PV module, charge controller, battery and electrical components
The housing shall be corrosion protected, lockable, ventilated, and tamper proof
The enclosure containing charge controller and battery shall be minimise heat transfer to the battery.
The streetlight head mounting at shall attach at the top of the pole and the array to be oriented 10˚ to the horizontal.

## Slide 18
Continue- Public streetlight systems
Separate lamp head, PV module and battery enclosure:
The solar array shall be mounted on an array mounting frame which attaches to the top of the pole and fixed angle of tilt of 10˚ to the horizontal.
The charge controller, battery and battery enclosure shall be shaded and out of direct sunlight. The battery enclosure shall be corrosion protected, lockable, ventilated, and tamper proof housing.
The battery and charge controller shall be mounted at the top of the pole in the shade of the solar array and the battery enclosure shall have a double skin to minimise heat transfer to the battery via the sun.

## Slide 19
PV Modules for public facilities
Certification Standards :
ICE 61215(2005-04) : Design qualification and type approval
Crystalline silicon terrestrial PV Modules
PV array consists of one or more Mono-crystalline or Poly-crystalline Modules
Thin film modules are not acceptable
Rated power of each modules shall be at least 75Wp (except of streetlights)
Only three standard sizes of modules shall be used to facilitate spares and parts management

## Slide 20
Continue- PV module for public facilities
All PV modules within an array shall be the same type
Each Module must be factory equipped with either weather-proof junction box or a sealed weather proof termination for safe and solid wiring connection
Crystalline Modules have a minimum of 36 cells connected in series for 12V batteries and 72 cells for 24V batteries
Rated output tolerance of PV modules shall be positive only. Negative tolerance are not allowed.
Warranty: (20) years
Modules shall produce at least 80% of its nominal rated output at STC for at least 20 years.

## Slide 21
Batteries for public facilities
Certification standards:
ICE 61427 Ed. 2.0(2004-05) ‘Secondary Cells and Batteries for Photovoltaic Energy Systems(PVES)
IEC 60896-11,Ed 1.0(2002): ‘Stationary lead-acid batteries’
IEC 60896-21 and 22 Ed 1(2004);’ Stationary lead-acid batteries’
Certificates or equivalent standards i.e IEEE, may be proposed by suppliers
Certificates for batteries will be accepted from same manufacturer and range, but of different capacity due to use of different numbers of plates

## Slide 22
Continue- Batteries for public facilities
Lead acid: deep-cycle, heavy-duty, tubular positive plate, with immobilized electrolyte and valve regulated operation (75% maximum loadshed DoD)
Lead acid: deep-cycle, heavy-duty, tubular positive plate, with vented and flooded electrolyte cell( 75% loadshed DoD)
Li-ion: deep-cycle, heavy-duty, sealed ( 90% maximum loadshed DoD)
Battery cycle life at 50% daily depth-of-discharge (DOD) must exceed 1,800 cycles when tested in terms of IEC 61427 Ed. 2.0

## Slide 23
Charge Controllers for public facilities
Certification standards
EC 62509 Ed.1: Performance and functioning of PV battery charge controllers
IEC 62109: Safety of power converters for use in PV power systems
IEC 62093 Ed. 1.0: Environmental reliability testing-Design qualification and type approval
IECEE standard charge controller -PVRS6A
Solid state photovoltaic charge controller
Pulse width modulated (PWM) regulation type

## Slide 24
Inverters for public facilities
Certification Standards :
IEC 62109 Safety of power converters for use in photovoltaic(PV )power systems.Part2: particular requirements for inverters.
IEC 61683 Ed. 2.0: Photovoltaic systems- Power conditioners-Procedure for measuring efficiency
IECEE,PVRS8A ‘Inverters for photovoltaic(PV) stand-alone systems’
For noise and emission , the following shall apply:
IEC CISPR 22 Radio disturbance characteristics-limits and methods of measurement

## Slide 25
Continue- Inverters
IEC 61000-4-2 Electromagnetic compatibility(EMC) Testing and measurement techniques-electrostatic discharge immunity test
IEC 61000-4-3 Electromagnetic compatibility (EMC) Testing and measurement techniques radiated, radio frequency, electromagnetic field immunity test.
Only inverters with sine-wave outputs
Only inverters with full galvanic isolation between DC and AC
Sine wave inverters shall generate a sine-wave output of 230VAC +/- 5% and frequency of 50Hz +/- 0.5%.
The real power(kW) output of the inverter shall not less than the rated kVA multiplied times 0.8(power factor).

## Slide 26
LED interior/exterior luminaries(AC and DC)
Certification Standards :
Illumination Engineering Society’s(IES)
IES-LM-79-08 Approved method of electrical and photometric measurements for solid state lighting products
IES-LM-80-08 Approved method for measuring lumen maintenance of LED light sources
LED lights only (AC LED , DC LED only for street lights)
For AC LED, Energy star(US,Canada), Australian Energy Rating for appliances and European Eco-label for light bulbs certifications are allowable.

## Slide 27
“Thank You for your attention ”